## Slide 1: 《Fundamentals of Electric Circuits》
G Q Wu
Email:gqwu@ysu.edu.cn
(please turn off your mobile phone!)

## Slide 2: Pre class instructions
Experiment：10%；
Materials：《电路原理》，清华大学出版社；
Reference materials：
  1《电路》，邱关源主编，高教出版社
  2《Electric Circuits》,James W. Nilsson,电子工业出版社
  3《Fundamentals of Electric Circuits》,Charles K. Alexander,机械工业出版社
CAA：Pspice,Multisim,Tina Pro,Cadence,Matlab

## Slide 3
1、Basic Circuit Principles
  ①Basic elements(R、L、C、Us、Is)
  ②Basic Laws(VCR、KCL、KVL)
  ③Methods of Analysis
  ④Circuit Theorem(ST、TNT)
2、Dynamic circuit Analysis(FO)
3、Sinusoidal Steady-State Analysis
4、Three-Phase Circuit
Course introduction

## Slide 4
1. Reference direction
3. Kirchhoff 's Law
key points：
Chapter 1
Circuit Models and Circuit Laws
2. Voltage-Current relationship

## Slide 5
1.1 Actual Circuit and Circuit Model
1. Actual Circuit
Function
a) transmission, distribution and conversion of electricity;
b) transmit and process electrical signals
Similarity
based on same circuit theory basis
The current path is connecting by some electrical equipment and components in a certain way , also called a network.

## Slide 6
It is composed of ideal circuit elements and can reflect the electromagnetic properties of actual circuits
2. Circuit Model
connecting wires
battery
switch
Light bulb
circuit diagram
Ideal circuit element
An ideal element having certain electromagnetic properties
circuit model

## Slide 7
Several basic circuit elements：
Resistor：
A device that consumes electrical energy.
Inductors：
A device that produces a magnetic field and
stores its energy.
Capactors：
A device that generates an electric field and
stores its energy.
Power source：
A device that converts other forms of energy
into electrical energy.

## Slide 8
Example:
3. Lumped parameter circuit
A circuit composed of lumped elements
Lumped conditions
d: dimensions of circuit elements
λ: working wavelength

## Slide 9
1.2 Reference Direction and Power
1. Current Reference Direction
Current
Current Intensity
regular directional movement of electric charge
the amount of charge passing through the cross-section of a conductor in unit time

## Slide 10
Direction
the direction of positive charge movement
Units
1kA=103A
1mA=10-3A
1  A=10-6A
A（Ampere）、kA、mA、A
Two possibilities for the actual direction of the current:

actual direction
actual direction

A
A
B
B
question:
When the current in a complex circuit changes with time, the actual direction is often difficult to judge.

## Slide 11
Current Reference Direction
i reference direction
randomly assume one direction of positive charge movement
A
B
i reference direction
i reference direction
i > 0
i < 0
actual direction
actual direction
Reference Direction and Actual Direction ：
A
A
B
B

## Slide 12
 arrow：
current reference direction: the direction of the arrow
 double subscript：
  e.g. iAB , current reference direction: A to B
i
A
B
iAB
A
B
Two representations of current reference direction ：

## Slide 13
Voltage Uab
unit：V 、kV、mV、V
2. Voltage Reference Direction
The voltage U between two points is the energy needed to move a unit charge from a to b
Electric Potential 
Charge q from circuit is moved to the reference point ( = 0) when the size of the electric field force to do work
Actual Voltage Direction
The direction of potential reduction

## Slide 14
Voltage Reference Direction
U
> 0
reference direction
U
+
–
+
actual direction
+
actual direction
reference direction
U
+
–
< 0
U

## Slide 15
(1) Arrows
(2) positive and negative polarity
(3) double subscripts
U
U
+
A
B
UAB
-
Three representations of voltage reference direction：

## Slide 16
U , I of components or branch use the same reference direction is called an associated reference direction. Conversely, it is called an nonassociated reference direction
associated reference direction
nonassociated reference direction
3. Associated Reference Direction
i
+
-
+
-
i
U
U

## Slide 17
note:
(1)Speccify reference direction;
(2)Do not change arbitrarily;
(3)“-”
A
B
A
B
i
Example:
＋
－
U
Reference direction of voltage and current as shown in the figure，Is the reference direction of voltage and current associated in part A and Part B?
answer： A: nonassociated；
B: associated.

## Slide 18
4. Electric Power
unit of power：W (Watt)
unit of energy： J (Joule)
The work done by the electric field force per unit time.

## Slide 19
5. Circuit Absorbed or supplied Power
u, i Reference direction associated
P=ui implies element is absorbed power
P>0 absorbed positive power (absorbed power )
P<0 absorbed negative power (supplied power)
P = ui implies element is released power
P>0 released positive power (supplied power)
P<0 released negative power (absorbed power)
u, i Reference direction nonassociated
+
-
i
u
+
-
i
u

## Slide 20
Example
Find the power absorbed or supplied to all circuit element：
U1=1V, U2= -3V,
U3=8V, U4= -4V,
U5=7V, U6= -3V
I1=2A, I2=1A,
I3= -1A
answer：
note:
In a complete circuit，supplied power＝absorbed power
5
6
4
1
2
3
I2
I3
I1
+
+
+
+
+
+
－
－
－
－
－
U6
U5
U4
U3
U2
U1
－
P4=U4I2=(-4)×1=-4W(supplied)
P5=U5I3=7×(-1)=-7W(supplied)
P6=U6I3=(-3)×(-1)=3W(absorbed)
P2=U2I1=(-3)×2=-6W(supplied)
P3=U3I1=8×2=16W(absorbed)
P1=U1I1=1×2=2W(supplied)

## Slide 21
1.3.1 Resistor
2. Linear time-invariant resistance element
symbol
R
resistor
Current limiting element
i
u
u ∝ i
1. Definition
voltage-current
characteristic
1.3 Resistor、Independent source、Dependent source

## Slide 22
Voltage Current Relation(VCR)
R ：resistance，unit： (Ohm)
Ohm's law
u
i
unit
G :conductance ，unit： S (Siemens)
u、i take the associated reference direction
R
u
i
+
－
Video presentation

## Slide 23
(2) nonassociated : “-”
note:
(3) memoryless and bidirectional
(1) Linear resistors R is constant
Then Ohm's law is written as
u  –R i i  –G u
Formula and reference direction must be used together!
R
u
i
+
-
Ohm’s Law

## Slide 24
3. Power and Energy
p  u i (–R i) i -i2 R
 u(–u/ R)  -u2/R (absorbed)
p  u i i2R u2 / R (absorbed)
Power：
R
u
i
+
-
R
u
i
+
-
Resistors absorbed power at all times

## Slide 25
Energy consumed by the resistance from t to t0:
R
i
u
+
–
4. Open-Circuit and Short-Circuit of resistance
Energy：
short-circuit
open-circuit
u
i

## Slide 26
On September 14, 2022, Shanghai enterprises achieved mass production of 14 nm advanced process scale, and breakthroughs were made in 90 nm lithography machine, 5 nm etcher, 12 inch large silicon chip, domestic CPU and 5G chip.
Superconducting quantum chip
Notes: 2022年9月14日，上海企业实现了14纳米先进工艺规模的批量生产，在90纳米光刻机、5纳米蚀刻机、12英寸大硅芯片、国产 CPU 和5G 芯片等领域取得了突破。

## Slide 27
1.3.2 Independent Source
circuit symbol
1. Ideal Voltage Source
definition
i
+
_
The voltage is constant, indepenent of its current

## Slide 28
(1) Constant voltage
(2) The current through the voltage source depends on the power and external circuit。
u
i
example:
R
i
-
+
external circuit
The voltage source cannot be short circuited!
VCR

## Slide 29
The power of the independent voltage source
（1） u , i nonassociated
+
_
i
u
+
_
+
_
i
u
+
_
supplied power
（2） u , i associated
absorbed power
P=usi

## Slide 30
Example:
+
_
i
+
_
+
_
10V
5V
Calculate the power of each element in the diagram
Solution:
supplied
absorbed
absorbed
P5V=usi=5×1=5W
P10V=usi=10×1=10W
P（supplied）＝P（absorbed）

## Slide 31
us
u
i
O
The actual voltage source
i
+
_
u
+
_
Internal resistance
VCR
A good voltage source
The actual voltage source shall not be short circuited！

## Slide 32
symbol
2. Ideal Current Source
definition
u
+
_
(1) Constant current
(2) Voltage between its two terminals of curent source depends on the power and external circuit。
VCR
u
i
The current is constant, indepenent of its voltage

## Slide 33
Example:
external circuit
Current source cannot be opened！
R
u
-
+

## Slide 34
The power of the independent current source
（1） u , i nonassociated
supplied power
（2） u , i associated
absorbed power
u
+
_
u
+
_
P=uiS

## Slide 35
Example:
Calculate the power of each element in the diagram.
answer:
(supplied)
(absorbed)
+
_
u
+
_
2A
5V
iS=2A
P2A=uiS=5×2=10W
P5V=uiS=5×2=10W
P（supplied）＝P（absorbed）

## Slide 36
is
u
i
O
Actual Current Source
Internal resistance
A good current source
u
+
_
i
The actual current source cannot be opened！

## Slide 37
1.3.3 Dependent Source
(controlled source )
An ideal dependent (or controlled) source is an active element in which the source quantity is controlled by another voltage or current.
symbol
+
–
controlled voltage source
1. definition
controlled current source

## Slide 38
(1) Current-Controlled Current Source ( CCCS )
 : Current amplification factor
2. Classification
four terminals elements
b i1
+
_
u2
i2
_
u1
i1
+
output：controlled source
input：control source

## Slide 39
g: Transfer conductance
(2) Voltage-Controlled Current Source ( VCCS )
u1
gu1
+
_
u2
i2
_
i1
+
(3) Voltage-Controlled Voltage Source ( VCVS )
u1
+
_
u2
i2
_
u1
i1
+
+
-
: Voltage amplification factor

## Slide 40
ri1
+
_
u2
i2
_
u1
i1
+
+
-
(4) Current-Controlled Voltage Source ( CCVS )
r : Transfer resistance
Example:
Circuit model

## Slide 41
3. Comparison
(1) The independent source voltage (or current) is determined by the source itself , while the controlled source voltage (or current) is determined by the control quantity.
(2) The independent source generates voltage and current in the circuit, while the controlled source only reflects the relationship between output and input.
Example:
IS=2A，U2=0.5U1，R1=5Ω，R2=2Ω，find I2。
solution:
+
-
U1
R1
+
-
U2
R2
I1
I2
IS

## Slide 42
1.4 Kirchhoff’s Laws
Kirchhoff’s current law( KCL )
Kirchhoff’s voltage law (KVL)

## Slide 43
1. Terms
A node is simply a point of connection of three or more branches. ( n )
b=3
a
n=2
b
+
_
R1
uS1
+
_
uS2
R2
R3
（1） Branch
The same current . (b)
i3
i2
i1
(2) Node

## Slide 44
A closed path.
A path between two nodes.
A loop that does not contain any branches.
l=3
+
_
R1
uS1
+
_
uS2
R2
R3
1
2
3
(3) Path
(4) Loop
(5) Mesh
The mesh is a loop，But the loop does not have to be a mesh.

## Slide 45
2. Kirchhoff’s Current Law (KCL)
output is“+”，so：
Example:
??
or

## Slide 46
1
3
2
Example:
sum：
note:
（1）Charge conservation and Current continuity ;
（2）The current reference direction .
KCL is applicable to closed surfaces containing multiple nodes.

## Slide 47
（2）Select the direction of the loop, clockwise or counterclockwise.
–U1–US1+U2+U3+U4+US4= 0
3. Kirchhoff ’ s voltage law (KVL)
I1
+
US1
R1
I4
_
+
US4
R4
I3
R3
R2
I2
_
U3
U1
U2
U4
（1）Calibrate the voltage reference direction of each element
U2+U3+U4+US4=U1+US1
or：
–R1I1+R2I2–R3I3+R4I4=US1–US4
or
or

## Slide 48
example:
a
Us
b
_
_
-
+
+
+
U2
U1
Note:
（1） The conservation of energy;
（2）The voltage reference direction .
Example1-4,1-5
KVL is applicable to hypothetical loop.

## Slide 49
4. Summary of KCL、KVL ：
(1) KCL is a linear constraint on the branch current and KVL is a linear constraint on the loop voltage.
(2) KCL and KVL are independent of the components that make up the branch.
(3) KCL shows that charge is conserved at each node; KVL embodies the conservation of energy.
(4) KCL and KVL are only applicable to lumped circuits.

## Slide 50
1.
2.
+
+
-
-
4V
5V
i =?
3.
+
+
-
-
-
4V
5V
1A
+
-
u =?
4.
3
3

## Slide 51
10V
+
+
-
-
1A
-10V
I =?
10
5.
4V
+
-
10A
U =?
2
6.
+
-
3A
I1
I
10V
+
+
-
-
3I2
U=?
I =0
5
7.
5
-
+
2I2
I2
5
+
-

## Slide 52
Solution:
10V
+
+
-
-
1A
-10V
I =?
10
5.
4V
+
-
10A
U =?
2
6.
+
-
3A
I
Solution:
I1

## Slide 53
10V
+
+
-
-
3I2
U=?
I =0
5
7.
5
-
+
2I2
I2
5
+
-
Solution:

## Slide 54
3
1
+
－
10W
5V
2
15W
20W
Given that 1,2, and 3 are resistors and their absorption powers are 10W, 15W, and 20W respectively, determine their resistance.
8.
9A
5A
4A
Solution:
R1=10/25=0.4Ω
R2=15/25=0.6Ω
R3=5/4=1.25Ω

## Slide 55
Homework：1-30、34、35、36